## Slide 1
ECET 250E
Camosun College
Electronics & Computer Engineering Technology
Linear Circuits 1
Week 4 | Chapter 4: Circuit Theorems
Mozhgan Bacon, PhD, P.Eng.
Fall 2026
Based on Fundamentals of Electric Circuits, 2026 Release — C.K. Alexander, M.N.O. Sadiku & S.J. Fredette (McGraw Hill)

## Slide 2: Overview
In this chapter, the concept of superposition will be introduced.
Source transformation will also be covered.
Thevenin and Norton’s theorems will be covered.
And Maximum Power Transfer.

## Slide 3: Linearity
Linearity in a circuit means that as current is changed, the voltage changes proportionally.
It also requires that the response of a circuit to a sum of sources will be the sum of the individual responses from each source separately.
A resistor satisfies both of these criteria.

## Slide 4: Superposition
If there are two or more independent sources there are two ways to solve for the circuit parameters:
  Nodal or mesh analysis.
  Use superposition.
The superposition principle states that the voltage across (or current through) an element in a linear circuit is the algebraic sum of the voltages across (or currents through) that element due to each independent source acting alone.

## Slide 6: Applying Superposition
Using superposition means applying one independent source at a time.
Dependent sources are left alone.
The steps are:
Turn off all independent sources except one source. Find the output (voltage or current) due to that active source using the techniques covered in Chapters 2 and 3.
Repeat step 1 for each of the other independent sources.
Find the total contribution by adding algebraically all the contributions due to the independent sources.

## Slide 10: Source Transformation
it is possible to transform a source from one form to another.
This can be useful for simplifying circuits.
The principle behind all of these transformations is equivalence.

## Slide 11: Source Transformation II
A source transformation is the process of replacing a voltage source vs in series with a resistor R by a current source is in parallel with a resistor R, or vice versa.

## Slide 12: Terminal Equivalency
These transformations work because the two sources have equivalent behavior at their terminals.
If the sources are turned off the resistance at the terminals are both R.
If the terminals are short circuited, the currents need to be the same.
From this we get the following requirement:

## Slide 13: Dependent Sources
Source transformation also applies to dependent sources.
But, the dependent variable must be handled carefully.
The same relationship between the voltage and current holds here:

## Slide 14: Source transformation rules
Note that the arrow of the current source is directed towards the positive terminal of the voltage source.
Source transformation is not possible when R = 0 for an ideal voltage source.
For a realistic source, R  0.
For an ideal current source, R = ∞ also prevents the use of source transformation.

## Slide 21: Thevenin’s Theorem
In many circuits, one element will be variable.
An example of this is mains power; many different appliances may be plugged into the outlet, each presenting a different resistance.
This variable element is called the load.
Ordinarily one would have to reanalyze the circuit for each change in the load.

## Slide 22: Thevenin’s Theorem II
Thevenin’s theorem states that a linear two terminal circuit may be replaced with a voltage source and resistor.
The voltage source’s value is equal to the open circuit voltage at the terminals.
The resistance is equal to the resistance measured at the terminals when the independent sources are turned off.

## Slide 23: Thevenin’s Theorem III
There are two cases to consider when finding the equivalent resistance.
Case 1: If there are no dependent sources, then the resistance may be found by simply turning off all the sources.

## Slide 24: Thevenin’s Theorem IV
Case 2: If there are dependent sources, we still turn off all the independent sources.
Now apply a voltage v0 (or current i0) to the terminals and determine the current i0 (voltage v0).

## Slide 25: Thevenin’s Theorem V
Thevenin’s theorem is very powerful in circuit analysis.
It allows one to simplify a circuit.
A large circuit may be replaced by a single independent voltage source and a single resistor.
The equivalent circuit behaves externally exactly the same as the original circuit.

## Slide 26: Negative Resistance?
It is possible for the result of this analysis to end up with a negative resistance.
This implies the circuit is supplying power.
This is reasonable with dependent sources.
Note that in the end, the Thevenin equivalent makes working with variable loads much easier.
Load current can be calculated with a voltage source and two series resistors.
Load voltages use the voltage divider rule.

## Slide 39: Norton’s Theorem
Similar to Thevenin’s theorem, Norton’s theorem states that a linear two terminal circuit may be replaced with an equivalent circuit containing a resistor and a current source.
The Norton resistance will be exactly the same as the Thevenin.

## Slide 40: Norton’s Theorem II
The Norton current IN is found by short circuiting the circuit’s terminals and measuring the resulting current.

## Slide 41: Norton versus Thevenin
These two equivalent circuits can be related to each other.
One need only look at source transformation to understand this.
The Norton current and Thevenin voltage are related to each other as follows:

## Slide 42: Norton versus Thevenin II
With VTH, IN, and (RTH=RN) related, finding the Thevenin or Norton equivalent circuit requires that we find:
The open-circuit voltage across terminals a and b.
The short-circuit current at terminals a and b.
The equivalent or input resistance at terminals a and b when all independent sources are turned off.

## Slide 55: Maximum Power Transfer
In many applications, a circuit is designed to power a load.
Among those applications there are many cases where we wish to maximize the power transferred to the load.
Unlike an ideal source, internal resistance will restrict the conditions where maximum power is transferred.

## Slide 56: Maximum Power Transfer II
We can use the Thevenin equivalent circuit for finding the maximum power in a linear circuit.
We will assume that the load resistance can be varied
Looking at the equivalent circuit with load included, the power transferred is:

## Slide 57: Maximum Power Transfer III
For a given circuit, VTH and RTH are fixed. By varying the load resistance RL, the power delivered to the load varies as shown.
You can see that as RL approaches 0 and ∞ the power transferred goes to zero.
In fact the maximum power transferred is when RL= RTH.

## Slide 65
© McGraw Hill LLC.
Because learning changes everything.®
www.mheducation.com